A combined application of laser tracker and Spatial Analyzer in Alignment and Survey of Hirfl-CSR

Guozhu Cai, Kaidi Man, Shengli Yang, Shaoming Wang, Wenjun Chen，Jiandong Yuan

IMP, 730000 Lanzhou, China

Abstract

With the new instruments come forth, the many portable 3D CMM, like laser tracker, etc. was widely applied to alignment and survey of accelerator. Now，the primary problem is how to use them more efficiently face to our alignment. SpatialAnalyzer (SA) is a traceable metrology 3D graphical software platform that can simultaneously communicate to virtually any number and type of dimensional measurement system like laser tracker etc, and perform complex analysis tasks. In the alignment and survey of our project CSR(Cooling Storage Ring), we operate the laser tracker to survey network, analysis and solve the results, and monitor adjust the position of magnets etc, all the tasks rely on the SA.  This method was more reliable than Insight4.0 we used before and can accomplish more tasks.

Key words: 3D survey network, SA , laser tracker

1. Introduction

The Cooling Storage Ring (CSR) is upgrade project of the Heavy Ion Research Facility in Lanzhou (HIRFL), it is as one of the national scientific projects in 9th five-year plan was put into operation in 2007.

It greatly enhanced the performance of HIRFL for those researches by using Radioactive Ion Beams and high-Z heavy ion beams in the fields of nuclear physics and atomic physics. The CSR consists of main ring (CSRm) and experimental ring (CSRe). The circumference of CSRm and CSRe is 161m and 128.8m respectively (see Figure. 1). Every year during the checking and fixing mouth in summer, we need survey control network in order to check the position of magnet and decide to if need to adjust position error of magnets.

Figure1. Layout of Hirfl-CSR

A Laser tracker provides a relatively fast, accurate and intuitive method of measuring large objects in industrial environments, now it was wide applied to alignment and survey of accelerator. API T3 is the newest laser tracker with compact shape and reliable performance. Formerly，we used the SMX tracker 4500 and its application--Insight 4.0 to measure tasks , but they were outdated after 8 years, so we must find new solution for our project.

SpatialAnalyzer (SA) is a traceable metrology 3D graphical software platform that can simultaneously communicate to virtually any number and type of dimensional measurement system like laser tracker etc, and perform complex analysis tasks.

2. Laser tacker measure 3D survey control network

It is necessary to build the 3D control survey network in the CSR for monitoring and aligning the magnets, Unified Spatial Metrology Network (USMN) brings answer to our measurement uncertainty issues, and the USMN is GUM compliant and meets ISO standard requirements. Some highlighted features list:

- Different weighting for different observation points and instruments.

- Considers instrument uncertainties and calculate point uncertainties.

- DOF (degree of freedom) freely definable.

- Using scale bars can constrain dimension error.

Following example is measurement of CSRm.

Firstly, like before, we measured all the net points, including the reference points on the magnets (8 reference points on every magnet were fiducialized previously) , 8 leveling net points, and the nets on the wall, in the 14 stations one by one, used bundle adjustment to link the both adjacent stations and close loop around ring finally.( the magnet layout of CSRm in Figure2, and the survey control network illustrated in Figure3)

Figure2. Layout of main ring in Hirfl-CSR

Figure3.  Illustration of surveyed CSRm

Secondly, Run the analysis of coordinate uncertainty in the USMN. Then choose all stations and solve it after trim outliers, the summary of the points error: overall RMS is 0.043 with 95.46% confidence interval(2.0 sigma). It is the outstanding result.

Thirdly, the level plane was created from 8 net points that corrected height with the known value measured by Digital Level from Leica DNA03, The 8 net points were measured by tracker too in the survey network, It solved how to decrease the deviation of height during building the 3D Control Survey Network.  The plane, which RMS is 0.068mm(Figure4),constructed by the 8 net points, and This plane  was used to construct a local frame to align the part frame.

Figure4.  Best-fit plane from 8 leveled net points.

Fourthly, When the 3D survey control network was built, any measurement on the Ring is convenient, each equipment, like magnet, hold the own part frame with different coordinate and rotated angle in the local Ring frame. In the SA, we can create the part frame for each equipment and change frame among them freely.

We can use the 3D survey control network to check and adjust the position of magnets.

3. Checking and fixing the position error of magnets

After located instrument beside the monitored magnet in the 3D survey control network depended on the nets around it, changed the live frame to this magnet part frame, the 8 reference points were measured on the magnet would be the actual data. an application of best-fit programmed by Matlab(also can do this in SA) can solve them with the actual data and the nominal data come from fiducialized magnet before. after solve it ,we can get the 7 parameters: DetlaX,  DetlaY,  DetlaZ,  RotatedX,  RotatedX,  RotatedZ and Scale in the nominal part frame  respectively, these parameters imply if the magnet need to be adjusted.

Each equipment need to check with the same method mentioned above.Figure5 and Figure6 illustrated the process respectively.

Figure5.  Illustration of locating the instrument in the network  after best-fit:

Figure6.  An example of actual data and nominal data of reference points on the magnet.

4. Best-fit position of magnets on orbit

In the SA, the best-fit transformation is powerful function, it not only can best-fit actual points to nominal points, but also can best-fit actual points to nominal 3D object/surface, or point clouds to object.

When we measured all adjusted Q-magnet tie to 3D survey control network. Each the center of Q-magnets will be used to best-fit the object of orbit, it was

simulated by the 0.01mm thin plane of boundary of orbit shape was built by Catia V5. After solved, every magnet error can be showed,  it is clear that we need to know deviation to orbit ultimately.

Figure7.  An illustration of best fitting orbit

5. Others useful function in the SA

The SA is power software in the survey, especially in the field of large dimension with high precision. Others the function is as well as very useful.

SA can drive almost all the portable measurement instrument and bundle adjustment for different instrument and stations.  we achieve the laser tracker API T3 and Leica total station TCA2003 worked together.

Measurement plan, it is an advanced programming language for automated measurement, analysis, reporting and archival processes.

Survey simulation, it is very useful function for measurement planning and precision estimation

6. Summary

It brings much help for us for implementing survey in the layout, measurement, analysis, report with SA.

I think, its strongpoint:

- Strong platform drive all kind of measurement instrument;

- Data analysis accords with GUM and ISO standard;

- Much functional module for all kind of tasks.

its shortcoming:

- Price and cost of maintenance is expensive;

- It’s not easy to understand operate the software

7. References

[1]	SPATIALANALYZER USER’S MANUAL，New River Kinematics, Inc.1.21.2008.Copyright 1996-2008 New River Kinematics

[2]	The J.W. Xia, W.L. Zhan, B.W. Wei et al,  “The heavy ion cooler-storage-ring project (HIRFL-CSR) at Lanzhou”,  Nuclear Instruments & Methods In Physics Research A 488 (2002) 11-2