## Slide 1: Experience Report with the Alignment Diagnostic System
Georg Gassner September 17th 2010

## Slide 2
Linac Coherent Light Source at SLAC
Injector (35º)
at 2-km point
Existing 1/3 Linac (1 km)
(with modifications)
Near Experiment Hall
Far Experiment
Hall
Undulator (130 m)
X-FEL based on last 1-km of existing 3-km linac
New e- Transfer Line (340 m)
1.5-15 Å
(14-4.3 GeV)
X-ray Transport Line (200 m)
UCLA

## Slide 3: Undulator System
Quadrupole
Hydrostatic
Leveling Sensor
3.4m undulator magnet
Wire Position
Monitor
CAM based 5 DOF
Motion control
X-translation
(in/out)
Sand-filled
Thermally Isolated
Supports

## Slide 4: Goal of the Alignment Diagnostic System
Question: Do we know how stable the LCLS tunnel and the
Undulator will be?
Answer: No, we don’t!
Advice: Install a girder position monitoring system…..
1
2
33
i
Undulator: 33 Girder, 132 m
X-pos
Y-pos
Resolution: < One Micrometer
Measurement duration: > Weeks, no drifts
Building Blocks: Hydrostatic Leveling System (HLS) for Y - direction. Experience: Used @ SLAC
Wire Position Monitors (WPM) for the X & Y direction.* Experience: FFTB @ SLAC
* Original design from DESY as contribution to the FFTB experiment at SLAC, 1991
... and track each girder relative to the Least Square Fit of all girders!

## Slide 5: Alignment Diagnostics System
WPM and HLS operates as one system, called
Alignment Diagnostic System, ADS
WPM measures:
X and Y- positions relative to two stretched wires
HLS measures:
Y - Positions relative to the water surface level
Common Task:
X & Y Positon monitoring of undulator segments
Resolution: < micrometer
Data rate: every minute
Operation: continous
1400 mm

## Slide 6: Results: Two days of tracking– no cam or stage movement
10 µm
2010/3/8 0:00
2010/3/10 0:00
2010/3/9 0:00
Hydrostatic leveling sensor readings - vertical

## Slide 7: Results: Two days of tracking– no cam or stage movement
10 µm
2010/3/8 0:00
2010/3/10 0:00
2010/3/9 0:00
Wire position sensor readings - vertical

## Slide 8: Results: Two days of tracking– no cam or stage movement
10 µm
2010/3/8 0:00
2010/3/10 0:00
2010/3/9 0:00
ADS response - vertical
Stretched wire
Undulator hall below ground

## Slide 9: Results: Two days of tracking– no cam or stage movement
10 µm
2010/3/8 0:00
2010/3/10 0:00
2010/3/9 0:00
Wire position sensor readings - horizontal

## Slide 10: Results: Two days of tracking– no cam or stage movement
10 µm
2010/3/8 0:00
2010/3/10 0:00
2010/3/9 0:00
ADS response - horizontal

## Slide 11: Results: normal operation – moving girders
10 µm
2010/9/8 17:37
2010/9/9 17:37
ADS response - vertical

## Slide 12: Problem (1): HLS time delay
Water takes several hours to settle if movement is big enough to require water to redistribute
Our pipes are mounted to the girder, if a girder moves all the water in the 4m pipe section has to redistribute

## Slide 13: Problem (2): Best fit solution
Positions are given in respect to reference line which is the best fit solution.
If one girder is moved deliberately this would change the reference line and indicate that all girders have moved.
Girder positions
Reference line

## Slide 14: Problem (2): Best fit solution
Positions are given in respect to reference line which is the best fit solution.
If one girder is moved deliberately this would change the reference line and indicate that all girders have moved.
Girder positions
Reference line

## Slide 15: Problem (2): Best fit solution
Positions are given in respect to reference line which is the best fit solution.
If one girder is moved deliberately this would change the reference line and indicate that all girders have moved.
Girder motions are communicated to the ADS system and taken into account in the adjustment
Girder positions
Reference line

## Slide 16: Results: normal operation – moving girders Quick response mode
10 µm
2010/9/8 17:37
2010/9/9 17:37
ADS response - vertical

## Slide 17: Results: normal operation – moving girders Quick response mode
200 µm
2010/9/8 17:37
2010/9/9 17:37
ADS response - vertical

## Slide 18: Summary
ADS achieved original goal of monitoring quadrupole position to the micrometer level
Add-ons:
  Cam/stage system motion is taken into account for reference line fit.
  Since girders are moved by tens of µm, a “quick response” algorithm to monitor the girder position short term had to be added.

## Slide 19
The End

## Slide 20: Introduction
Text goes here.
  Since 2009 an Alignment Diagnostic System (ADS) has been operating at the undulator of the new Linac Coherent Light Source at SLAC National Laboratory. The undulator spans a distance of 132 meters and is structured into 33 segments. Each segment is equipped with four hydrostatic leveling sensors and three wire position monitors. This report describes the set up and reflects long time experience gained with ADS.

## Slide 21: Wire Position Monitor *
Monitor Length 74 Millimeter
Monitor GAP 8 Millimeter Square
* Original design from DESY as contribution to the FFTB experiment at SLAC, 1991

## Slide 22: LCLS - WPM system sensitivity – e.g. response on social noise -
15th
19.6Hz
1st
1.3Hz
2nd
2.6Hz
3rd
3.9Hz
4th
5.2Hz
5th
6.5Hz
6th
7.8Hz
7th
9.1Hz
8th
10.4Hz
9th
11.8Hz
10th
13.1Hz
11th
14.4Hz
12th
15.7Hz
13th
17.0Hz
14th
18.3Hz
2nd and higher even harmonics missing
Monitor at the middle of the 140 m wire
Monitor outside the middle of the 140 m wire
3.925 Hz: 0.027 µm
3.95 Hz: 0.0086 µm
18.375Hz: 0.0046 µm
X
Y
X
Y
2nd and higher even harmonics visible
Frequency analysis of the 140 m stretched wire. - 40 seconds of data acquisition -

## Slide 23: Integration of ADS to girder: Artist view
Drawing: Courtesy by Scott Doran, ANL
Ultra sonic
Capacitive
Capacitive
Capacitive
WPM
WPM