## Slide 1: Latest Results from the CLIC Geodetic Studies
Mark Jones, CERN
Sébastien Guillaume, ETH Zurich / CERN
Julien Boerez, Université de Strasbourg / CERN

## Slide 2: Outline
Introduction
Determination of a Precision Geoid
Modelling the Tidal and other Time Variable Effects on HLS Measurements
Conclusions

## Slide 3: Geodetic Studies
Feasibility Study for CLIC
Pre-Alignment tolerance
  ± 10 [mm] over 200 [m] (3s)
Knowledge of gravity field essential
  High precision geoid model
  Tidal and other periodic or non-periodic effects
  Particularly important for HLS
    CLIC Metrology Reference Network
Two doctoral research projects in progress
  Sebastien Guillaume and Julien Boerez

## Slide 4: CLIC Geodetic Requirements
Instantaneous equipotential surface at level of HLS & Instantaneous shape of the Earth along the surface where the HLS / Accelerator is installed
  In Euclidean space
  As a function of time
  With a relative precision of a few microns over 200 m
Earth’s gravity potential modelled by applying Newton’s Universal Law of Gravitation and his Second Law of Motion for a point P(x, y, z), considering
  Earth’s mass distribution
  Earth’s motion within our quasi-inertial solar system

## Slide 5: Earth’s Instantaneous Gravity Potential
Time independent elements define quasi-static part of the Earth’s gravity potential
Time dependent
Time independent
          r = distance from P(x,y,z) to dV
          r = density of dV
          dV = differential volume element
          w = Earth’s rotation angular velocity
          R = Earth’s radius
          j = latitude of P(x,y,z)

## Slide 6: Disturbing Potential
Can reformulate
To give
  Term U(x, y, z) is a known, perfect, mathematical potential field
  Term T(x, y, z) is a disturbing potential
    Potential field induced by non-modelled density anomalies
Disturbing potential cannot be modelled accurately
  Elements of derivatives can be observed
  Only astronomical levelling could meet CLIC tolerance
    Integrate Earth’s surface deflections of the vertical, e
Geometrical variations of the disturbing potential at level Htnl
Orthometric correction
(gravity measurements)

## Slide 7: Measurement Campaign
TZ32 tunnel
  ~850 long, ~80 m underground
Gravity Measurements
  Relative Gravimeter Scintrex CG-5
  Absolute Gravimeter FG-5
    Swiss Federal Office of Metrology (METAS)
  Profiles at Surface (every 10 m) and in Tunnel (every 5 m)
Deflection of the Vertical Measurements
  DIADEM (ETHZ)
  AURIGA software (University of Hannover)
  Measurement every 10 m
Jura mountains
LHC
TZ32
N

## Slide 8: Gravity Measurements
Absolute
FG-5
Relative
Scintrex CG-5

## Slide 9: Astro-Geodetic Measurements
DIADEM
Component | # type | Characteristic
Optic | 1x Mirotar | f=1020 mm D=200 mm
CCD camera | 1x Apogee Alta | 2184x1472 pixel, 6.8x6.8 microns, 16 bits
GPS timing | 1x ublox | precision: < 0.1 milisecond
Tiltmeters | 2x Wyler Zerotronics | range: +/- 3600'', precision: 0.15''
 | 4x Lippmann | range: +/- 200'', precision: <0.05''
Digital Focuser | 1x FLI PDF | range: 0-8.9 mm, resolution: 1.3 microns
Automation | 3x eletric cylinders | 
 | 5x servo motors | 
DAQ and Control | 2x computers | 

## Slide 10: Deflections of the Vertical

## Slide 11: Variation of the Disturbing Potential

## Slide 12: Next Steps
Confirm and improve measurement results
  Complementary astro-geodetic measurements
  Deeper analysis of gravimetric measurements
Try to show what we should expect to find in the real gravity signal
  Improved mass models taking into account local geological and hydrological information
  Stochastic simulations of the gravity field

## Slide 13: Tide Potential
Gravity potential equation
Let us now consider the Tidal Potential
  Caused by relative motions of different bodies in our solar system (mainly Sun and Moon)
  Different effect on different instruments
  Each type of instrument is modelled by specific Love numbers
Time dependent
Time independent

## Slide 14: Perturbing Phenomena
Love numbers define the tidal effects for a perfect mathematical model of the Earth
Model perturbed at different scales by various phenomena
  geological structure of ground, topography
With a sufficient number of continuous measurements small corrections to the mathematical model can be calculated
  These corrections probably only apply to the installed HLS providing the measurement signal
There are other perturbing phenomena for an HLS too
  E.g. oceanic load, hydrological load, cavity effects

## Slide 15: Hydrostatic Levelling System
An HLS (a tiltmeter) is affected by the change in the Earth’s crust and the measured water surface
  Love number combination, g = 1 + k – h
HLS_1
HLS_2
H-Water_1
H-Air_2
H-Water_2
dH
Earth’s Crust
Equipotential Surface
H-Air_1
Δ1
Δ2
dH = H-Air_1 – H-Air_2 – Δ1 – Δ2

## Slide 16: Tilts and Deformations
In the context of accelerator alignment the difference between a tilt and a deformation is very important
The goal is to separate out the two from the raw measurement signal

## Slide 17: Raw HLS Measurement Signal
TT1 Tunnel
Chart: HLS readings

## Slide 18: Eterna Package
Major tool for analysis and prediction of tidal effects
  Developed by Prof.Dr.-Ing H.-G. Wenzel in the 1990’s
  Different tidal potential catalogues available
  Many programs included in the Eterna 3.30 Package
    ANALYZE program – for analysis of earth tide observations
      Compares raw measurements against theoretical tide models
      Determines modified tide parameters
        New amplitude and phase shift parameters to predict future measurements
    PREDICT program – computation of synthetic model tides
      Standard model, or results from ANALYZE
Main tool used for our research

## Slide 19: HLS Network Analysis
Standard processing technique using Eterna
  Analysis of 2.5 month dataset
  Analysis values used to predict tides for later 3 week period
Predicted tides and some load signals* removed from raw HLS signal
But we cannot distinguish between periodic signals in raw measurements
  We need to separate some of them!
* Kindly provided by J.P. Boy, NASA GSFC

## Slide 20: Analysis Results

## Slide 21: Analysis Results

## Slide 22: Analytical Prediction
PREDICT program used to determine theoretical HLS tide signal
Predicted tides and all other known signals removed from raw HLS signal
This gives us an isolated ground deformation signal
We don’t know if he residual signal gives only local deformations!

## Slide 23: Prediction Results

## Slide 24: Prediction Results

## Slide 25: Next Steps
Need a different approach to meet specific needs of accelerator alignment
  Isolate local tilt signal and local deformation signal
Another possibility using ANALYZE program
  Need to determine models for as many phenomena as possible
  Remove all modelled signals from raw measurement signal
  Use sensor at one end of HLS and pair it up with each of the other sensors in turn
  Use results from end point sensors as base signal
  Remove signal from other analysed sensor pairs
  Remaining signals should represent relative movements of intermediate sensors

## Slide 26: Conclusions
Two research projects launched to address geoid and HLS issues from CLIC Feasibility Study and LHC installation
  Both projects in final year
800 metre tunnel selected for Geoid Precision study
  Campaigns of astro-geodetic and gravity measurements
  Modifications to zenith camera (DIADEM) to improve precision
  Initial results very promising
    Further work required to confirm results
Improved precision of DIADEM confirmed in difficult field conditions

## Slide 27: Conclusions
Two approaches tried to model tidal and other effects on HLS measurements
  Disadvantanges to both methods
Need a new approach to meet the specific requirements of accelerator alignment
  Multiple sensors on each network, looking to isolate local deformations and tilts
  Analysis is now in progress
Still some phenomena to take into account
Need to apply results to LHC networks and implement corrections

## Slide 28: Thank you for your attention